## Slide 1: Steps to programming the Seeed Studio XIAO SAMD21

## Slide 2: The Arduino IDE
The first step is to download and install the Arduino IDE for your operating system which can done from here:
https://www.arduino.cc/en/software
Generally, you can skip the various donation and email subscription options and press the “Just Download” buttons.

## Slide 3
Create a folder on your computer named: XIAO_Scope_pwm_awg
Download this file to that new folder: https://github.com/damercer/Arduino-Scopes/blob/main/XIAO/XIAO_Scope_pwm_awg/XIAO_Scope_pwm_awg.ino
In the (newly installed) Arduino IDE, pull down file to Open and open this INO file.

## Slide 4: In the IDE, pull down File to Preferences and click on the “Additional URLs” button.

## Slide 5: Copy and paste the following URL into the edit window and click OK. https://files.seeedstudio.com/arduino/package_seeeduino_boards_index.json
1
Click OK to accept this preference change.
2
3

## Slide 6: Open the Boards Manager and type “Seeed SAMD” in the Search bar and click INSTALL.
1
2
3
Boards Manager
Search
Install

## Slide 7: Plug the board into a USB port.
The green Power LED should be on.
Note: A new board fresh from the factory will probably be running the “Blink” program where the orange LED slowly blinks.

## Slide 8: Select the board from the board manager.
Check Mark Here

## Slide 9: Select the COM port for the Arduino. (Your port number may vary.)
Check Mark Here

## Slide 10: Confirm port selection in the lower right-hand corner of the IDE.

## Slide 11: Click on the right pointing arrow to compile and upload the software to the board.

## Slide 12: Confirmation of the upload.

## Slide 13
Confirm Board is functioning.
1
1- In the Arduino IDE, in the upper right corner, click on the icon that looks like a circle with a dot to open the serial monitor.
3- The board will respond, confirming that the code is loaded and running,
3
2- Type a capital I (eye) + Enter in the text entry line which appears in the middle of the screen.
2
Just the Green Power LED should be on.
Note: The Blue LED will flash whenever the PC communicates with the board.

## Slide 14: The XIAO SAMD21 board is now programmed to work with Universal ALICE GUI.